## Slide 1
Power Conscious Sensor-based Remote Home Monitoring System through IoT
Ali Attaran ENGR 844 Project
Professor Dr. Xiaorong Zhang
May 2017

## Slide 2
Flow chart
Temperature sensor
Light sensor

## Slide 3
2cm
Temperature sensor Interface (1)
Time (S)
Pin E2 (V)
300m
180m
320m
210m
240m
290m
210m
1 2 3 4 5 6 7
PE2
TMP36
+3.3V
1
2
3
Launchpad
PE1
FAN
+12V
150Ω
R1
PN2222A
For example at 180mV, ADCdata is (4096x180mV)/3300mV=223, So ADCdata will be 233 when temp sensor output is 180mV
At 70C, PE2 voltage will be
(70-25)X10mV+750mV=1100mV

## Slide 4
Temperature sensor Interface (2)
PE2
TMP36
+3.3V
1
2
3
Launchpad
PE1
FAN
+12V
150Ω
R1
PN2222A

## Slide 5
Acknowledge Flag
Read Voltage on PB6
Is Voltage
Vcc?
No
Yes
Turn On the LED
Turn Off the LED
Launchpad
PB7
R3 = 150Ω
LED
R2 = 39Ω
LDR
PB6
3.3V
Light sensor Interface
When the light is on, Vout to be 3.3.
R high = 2MOhm
R low = 4kOhm

## Slide 6
Nokia 5110 LCD Interface
'0' is ASCII 0x30
'1' is ASCII 0x31
'2' is ASCII 0x32
and so on.

## Slide 7
Launchpad
PC7
PC6
GND
Rx
Tx
GND
PC
USB cable
UART to USB converter (CP2102 USB to TTL)
UART 3
PuTTY Interface
2
8
.
7
6
°
C
UART TX buffer
28.76 °C
UART buffers

## Slide 8
GSM SIM900A Modem Interface

## Slide 9
Complete schematic